PART 1  GENERAL

1.01	SECTION INCLUDES

A.	Temporary Erosion and Sediment Control Measures.

1.02	RELATED SECTIONS

A.	Section 015700 – Temporary Controls

1.03	REFERENCES

A.	Washington State Department of Transportation (WSDOT) Standard Specifications for Road, Bridge, and Municipal Construction (current edition).

1.04	SUBMITTALS

A.	Catch Basin Insert product data.

1.05	QUALITY ASSURANCE

A.	The Owner will provide weekly inspections of the installed erosion control measures to ensure they’re functioning properly.  The contractor shall repair any deficiencies within 24 hours of being made aware.

PART 2  PRODUCTS

  - TEMPORARY EROSION AND SEDIMENT CONTROL MEASURES

- Storm Drain Inlet (Catch Basin) Protection:  Storm drain inlet protection shall conform to the details shown on the Drawings.  Geotextile fabric shall meet the requirements of the WSDOT Standard Specifications Table 1 for moderate survivability, and the minimum filtration properties of Table 2, in Section 9-33.2.

PART 3  EXECUTION

3.01	EXAMINATION

A.	Examine site to confirm location of erosion control measures as shown on the drawings will prevent sediment laden runoff from leaving the site.

3.02	TEMPORARY EROSION AND SEDIMENT CONTROL MEASURES INSTALLATION

A.	Storm Drain Inlet Protection:  Install catch basin inserts per manufacturer's instructions.  Inserts shall be installed where shown on the plans.

3.03	TEMPORARY EROSION AND SEDIMENT CONTROL MEASURES MAINTENANCE

A.	Maintenance required due to improper installation shall be fixed by the Contractor at no additional cost to the Owner.

B.	All erosion and sediment control measures shall be maintained by the Contractor for the life of the project.  Any labor and equipment required to maintain the functionality of the TESC measures for the life of the contract shall be the responsibility of the Contractor.

C.	Sawcutting shall be done with water to prevent dust and the resulting slurry is to be vacuumed up immediately.

D.	Access to the site shall be from the existing paved access from Highway 101 or Hooker Road.  Construction traffic shall be limited to existing paved surfaces to the greatest extent feasible to prevent trackout from the site.  Any trackout onto public roadways shall be cleaned up immediately.

End of Section 01 57 13