# PART 1 GENERAL

  - SECTION INCLUDES

- Sealants and joint backing.

  - REFERNCE STANDARDS

- ASTM C 834 – Standard Specification for Latex Sealants; 2005.

- ASTM C 920 – Standard Specification for Elastomeric Joint Sealants; 2005.

- ASTM C 1193 – Standard Guide for Use of Joint Sealants; 2009.

- ASTM D 1667 – Standard Specification for Flexible Cellular Materials—Poly(Vinyl Chloride) Foam (Closed-Cell); 2005.

  - SUBMITTALS

  - See Section 01300 – Administrative Requirements, for submittal procedures.

  - Product Data: Provide data indicating sealant chemical characteristics, performance criteria, substrate penetration, limitations, and color availability.

  - Manufacturer’s Installation Instructions: Indicate special procedures, surface preparation, and perimeter conditions requiring special attention.

  - QUALITY ASSURANCE

- Manufacturer Qualifications: Company specializing in manufacturing the Products specified in this section with minimum three years documented experience.

  - FIELD CONDITIONS

  - Maintain temperature and humidity recommended by the sealant manufacturer during and after installation.

  - WARRANTY

- Correct defective work within a five year period after Date of Substantial Completion.

- Warranty:  Include coverage for installed sealants and accessories which fail to achieve airtight seal and watertight seal, exhibit loss of adhesion or cohesion, or do not cure.

# PART 2 PRODUCTS

  - SEALANTS

- General Purpose Exterior Sealant: Acrylic, solvent release curing; ASTM C 920, Grade NS, Class 12-1/2, Uses M, G, and A; single or multi-component.

  - Color: Standard colors matching finished surfaces.

  - Applications: Use for:

    - Joints between concrete and other materials.

    - Joints between metal frames and other materials.

    - Other exterior joints for which no other sealant is indicated.

- Exterior Metal Lap Joint Sealant: Butyl or polyisobutylene, nondrying, nonskinning, noncuring.

  - Applications: Use for:

    - Concealed sealant bead in sheet metal work.

    - Concealed sealant bead in siding overlaps.

- General Purpose Interior Sealant: Acrylic emulsion latex; ASTM C 834, Type OP, Grade NF single component, paintable.

  - Color: Standard colors matching finished surfaces.

  - Applications: Use for:

    - Interior wall and ceiling joints

    - Joints between door and window frames and wall surfaces.

    - Other interior joints for which no other type of sealant is indicated.

  - ACCESSORIES

- Primer: Non-straining type, recommended by sealant manufacturer to suit application.

- Joint Cleaner: Non-corrosive and non-staining type, recommended by sealant manufacturer; compatible with joint forming materials.

- Joint Backing: Round foam rod compatible with sealant; ASTM D 1667, closed cell PVC; oversized 30 to 50 percent larger than joint width.

- Bond Breaker: Pressure sensitive tape recommended by sealant manufacturer to suit application.

# PART 3 EXECUTION

3.01	EXAMINATION

- Verify that substrate surfaces are ready to receive work.

- Verify that joint backing and release tapes are compatible with sealant.

  - PREPARATION

  - Remove loose materials and foreign matter that could impair adhesion of sealant.

  - Clean and prime joints in accordance with manufacturer’s instructions.

  - Perform preparation in accordance with the manufacturer’s instructions and ASTM C 1193.

  - Protect elements surrounding the work of this section from damage or disfigurement.

  - INSTALLATION

- Perform work in accordance with the sealants manufacturer’s requirements for preparation of surfaces and material installation instructions.

- Perform installation in accordance with ASTM C 1193.

- Measure joint dimensions and size joint backers to achieve width-to-depth ratio, neck dimension, and surface bond area as recommended by manufacturer, except where specific dimensions are indicated.

- Install bond breaker where joint backing is not used.

- Install sealant free of air pockets, foreign embedded matter, ridges and sags.

- Apply sealant within recommended application temperature ranges. Consult manufacturer when sealant cannot be applied within these temperature ranges.

- Tool joints concave.

  - CLEANING

- Clean adjacent soiled surfaces.

# END OF SECTION