# PART 1 GENERAL

  - SECTION INCLUDES

- Hardware for exterior doors.

- Thresholds.

- Weather-stripping, seals and door gaskets.

  - RELATED REQUIREMENTS

- Section 081113 – Hollow Metal Doors and Frames

  - REFERNCE STANDARDS

- ANSI/IC A117.1 – American National Standards for Accessible and Usable Buildings and Facilities; International Code Council; 2003.

- DHI (LOCS) – Recommended Locations for Architectural Hardware for Standard Steel Doors and Frames; Door and Hardware Institute; 2004.

- DHI WDHS.3 – Recommended Locations for Architectural Hardware for Flush Wood Doors; Door and Hardware Institute; 1993; also in WDHS-1/WDHS-5 Series, 1996.

- NFPA 80 – Standard for Fire Doors and Fire windows; National Fire Protection Association; 2007.

- UBC Std 7-2, Part II – Test Standard for Smoke and Draft-Control Assemblies; International Conference of Building Officials; 1997.

- UL (BMD) – Building Materials Directory; Underwriters Laboratories Inc.; current edition.

  - ADMINISTRATIVE REQUIREMENTS

- Coordinate the manufacture, fabrication and installation of products onto which door hardware will be installed.

  - SUBMITTALS

  - Finish Hardware Schedule:

    - Provide detailed hardware schedule, listing each door opening separately. Include two copies of catalog cuts for each item proposed to be used on this project.

  - Shop Drawings:

    - Indicate locations and mounting heights each type of hardware, schedules, catalog cuts, electrical characteristics and connection requirements.

    - Submit manufacturer’s parts list and templates.

  - Maintenance Data: Include data on operating hardware, lubrication requirements, and inspection procedures related to preventative maintenance.

  - QUALITY ASSURANCE

- Hardware Supplier Qualifications: A recognized distributor who has been furnishing hardware in the same area as the project for a period of not less than 5 years and has successfully completed projects similar in type and scope.

- Hardware Supplier Personnel: Employ an Architectural Hardware Consultant (AHC) to assist in the work of this section.

- The Hardware Supplier shall be a factory authorized distributor of the material provided and shall maintain a stock and parts inventory of all standard items supplied on the project for future service to the Owner.

  - DELIVERY, STORAGE AND HANDLING

- Package hardware items individually; label and identify each package with door opening code to match hardware schedule.

  - COORDINATION

- Coordinate the work with other directly affected sections involving manufacture or fabrication of internal reinforcement for the door frame.

- Furnish templates for door and frame preparation.

- Sequence installation to ensure utility connections are achieved in an orderly and expeditious manner.

- Coordinate Owner’s keying requirements during the course of the Work.

  - MAINTENANCE

  - Provide special wrenches and tools applicable to each different or special hardware component.

  - Provide maintenance tools and accessories supplied by hardware component manufacturer.

# PART 2 PRODUCTS

  - MANUFATURERS

- Hinges: Stanley Hardware or Precision.

- Locks and Latch Sets: Schlage Lock Co.

- Cylindrical Lock Sets: Schlage Lock Co.

- Mortise Lock Sets: Schlage Lock Co.

- Substitutions: See Section 01600 – Product Requirements

  - MATERIALS

- Hardware Finish per Owner,___________________.

  - GENERAL REQUIREMENTS FOR DOOR HARDWARE PRODUCTS

- Provide components that comply with the following:

- ANSI/ICC A117.1, American National Standard for Accessible and Usable Buildings and Facilities.

- Products Requiring Electrical Connection: Listed and classified by UL as suitable for the purpose specified and indicated.

- Finishes: Identified in schedule at end of section.

# PART 3 EXECUTION

3.01	EXAMINATION

- Verify that doors and frames are ready to receive work and dimensions are as indicated on shop drawings.

- Verify that electric power is available to power operated devices and of the correct characteristics.

  - INSTALLATION

  - Install hardware in accordance with manufacturer’s instructions and applicable codes.

  - Use templates provided by hardware item manufacturer.

  - Install hardware on fire-rated doors and frames in accordance with applicable codes.

  - Mounting heights for hardware from finished floor to centerline of hardware item:

- For steel doors and frames: Comply with DHI “Recommended Locations for Architectural Hardware for Steel Doors and Frames.”

- For wood doors: Comply with DHI “Recommended Locations for Architectural Hardware for Wood Flush Doors.”

  - FIELD QUALITY CONTROL

- Provide an Architectural Hardware Consultant to inspect installation and certify that hardware and installation ha been furnished and installed in accordance with manufacturer’s instructions and as specified.

  - ADJUSTING

- Adjust work under provisions of Section 01700.

- Adjust hardware for smooth operation.

  - PROTECTION

- Protect finished Work under provisions of Section 01700.

- Do not permit adjacent work to damage hardware or finish.

- Refer to Door Types and Schedule on Drawings.

- Coordinate electrical requirements for electric strikes at entry doors with Electrical Subcontractor.

# END OF SECTION