PART 1  GENERAL

1.01	INCLUDED SECTIONS

A.	Quality Assurance

B.	Grading Tolerances

C.	Disposal.

D.	Field Quality Control.

1.02	RELATED SECTIONS

A.	Section 311110 - Clearing and Grubbing

B.	Section 312300 – Excavation and Fill.

1.03	REFERENCES

A.	Washington State Department of Transportation (WSDOT) Standard Specifications for Road, Bridge, and Municipal Construction (current edition).

1.04	SUBMITTALS

A.	Soil Sterilant product data.

B.	Soil Sterilant MSDS.

C.	Soil Sieve Analysis of subgrade material within building pad and parking lot area.

1.05	QUALITY ASSURANCE

A.	Perform work of this section in accordance with Division 2 of the WSDOT Standard Specifications.

PART 2  PRODUCTS

A.	Soil Sterilant:  Soil Sterilant shall be a commercial product containing sodium chlorate or borate which has been proven effective under local conditions and is acceptable under state and local codes.

PART 3  EXECUTION

3.01	EXAMINATION

A.	Verify that all trees, vegetation and organic soils have been removed within the excavation area prior to beginning work.

B.	Inspect erosion control measures to ensure proper installation prior to beginning work.

C.	Contractor shall have a certified testing laboratory perform modified proctor test on representative sample of subgrade material.

3.02	PREPARATION

A.	Clear and Grub per Section 311100.

B.	Demolition per Section 024100

3.03	GRADING

A.	The Contractor shall grade site and prepare subgrade for asphalt roadway, curbs, and building pads per Section 2-06.3 of the WSDOT Standard Specifications.

3.04	TOLERANCES

- The Contractor shall bring grades within the following tolerances:

- Finish Subgrade shall be within 0.10 foot of design grade in non-structural areas.

- Finish Subgrade shall be within 0.05 foot of design grade in structural areas.

3.05	SOIL STERILANT

A.	Soil sterilant shall be applied under all asphalt pavement and concrete gutters.

B.	Apply soil sterilant according to manufacturer's instructions.

3.06	QUALITY CONTROL

A.	Once grading and preparation of subgrade is complete the subgrade will be field tested with a proof roll witnessed by the Engineer or Engineer's representative. Subgrade shall be firm and unyielding.  If a “soft spot” is witnessed by the Engineer, the unsuitable material shall be over excavated and structural fill shall be used to replace.  See specification section 312300 for procedure of installing and compacting fill.

End of Section 31 22 00